Sawyer Test

Name:

- Chain Saw fuel is made up of 	 .

- Unleaded gasoline and an additive to increase the octane rating

- Bar and chain oil and two cylinder oil

- Two cycle engine oil and unleaded gasoline

2.	The main role of the swamper is to 	.

- Ensure that all necessary PPE is worn while working.

- Minimize safety hazards such as kickback, pushback, and overreaching.

- Assist the sawyer by removing cut limbs and branches.

3.	The most dangerous area of the chainsaw bar is 	.

4.	This is the most dangerous area (see above) of the bar because 	.

- This area is likely to get caught in a bind or cause pull-in.

- It has the potential to cause kickback when caught or pinched.

- It is most likely to strike the ground or the sawyer’s left thigh.

5.  Name one or more maintenance tasks performed at least daily.

6.  Adding oil to the fuel mixture is 	.

- …vitally important, neglecting to do so can ruin a saw in minutes.

- …a good idea, otherwise the saw can overheat in warm weather.

- …suggested when breaking in a new chain.

7.  List three pieces of sawyer PPE.

8.  Chainsaws are powered by a 	.

- Two-cycle engine.

- Four-cycle engine.

- Two-cylinder engine.

9.  A properly sharpened chainsaw should produce 	.

  - Almost no woodchips at all.

  - Only very fine sawdust.

  - Large woodchips or shavings.

10.  If your saw tends to cut curving to one side you conclude that 	.

- The teeth have been sharpened unevenly.

- The chain needs to be tightened

- The bar and chain oil has run out.

11.  The part of the chain tooth that you sharpen is 	.

12.  The two major forces constantly acting on any tree are 	.

- Push-back and pull-in.

- Tension and compression.

- Binding and bucking.

13.  “If the axe is dull, and one does not sharpen the edge, then he must use more strength; but 	__________ brings success.”

14.  When cutting up this tree you need to be aware that 	.

- Cutting into the top of the log will result in the bar binding due to compression.

- Cutting into the bottom of the log will result in the bar binding due to compression.

- Tension and compression do not apply in this situation because one end of the tree is suspended.

15.  In this situation the chainsaw bar will 	.

  - Bind when cutting into either side of the log and wedges will be needed.

  - Bind when cutting into the bottom of the log because of tension.

  - Bind when cutting into the top of the log because of compression.

16.  Two key character qualities the Swamper should have are _______and ______?

- Alertness

- Generosity

- Caution

What did you learn in this course that will be helpful to you in serving others, in chainsaw work, or deployments?